## Slide 1: Island Park Reservoir Bathymetric Map
Process | Results | Application
Dr. Jack McLaren | Aquatic Ecology Program Manager
IDEQ Water Quality Workshop | March 2025

## Slide 2: Takeaways
Process: The HFF made a digital elevation model of Island Park Reservoir with simple tools

## Slide 3: Takeaways
Process: The HFF made a digital elevation model of Island Park Reservoir with simple tools
Results: useful, but resulting map and statistics area subject to measurement error

## Slide 4: Takeaways
Process: The HFF made a digital elevation model of Island Park Reservoir with simple tools
Results: useful, but resulting map and statistics area subject to measurement error
Application: Disseminating real-time information about water levels and water quality has proven popular and useful for recreation and science

## Slide 5: Process
Lowrance GPS sonar & small boat
June-July 2017
  2.5” maximum difference between days
  ~1 inch above or below full pool

## Slide 6: Process
200 m grid perpendicular to flow lines
Each point has depth and location data

## Slide 7: Process
Converted from .sL2 data (Lowrance proprietaray) to .gpx with conversion tool

## Slide 8: Process
R code
  clean datapoints, subsample, calculate elevations
  NAVD correction from MSL

## Slide 9: Process
Add subsample of surrounding 10 m DEM (USGS)
Add points representing the full-pool shoreline (6303 ft MSL)

## Slide 10: Process
Add subsample of surrounding 10 m DEM (USGS)
Add points representing the full-pool shoreline (6303 ft MSL)

## Slide 11: Process
Knit into single dataset
621,585 datapoints (399,667 within the lake)
Removed data from ingoing/outgoing trips + obvious erroneous data

## Slide 12: Process
QGIS
  B-spline interpolation to create DEM surface

## Slide 13: Process
QGIS
  B-spline interpolation to create DEM surface
  Use DEM surface to create contours

## Slide 14: Process
QGIS
  B-spline interpolation to create DEM surface
  Use DEM surface to create contours
  Symbology, roads, access points, etc.

## Slide 15: Process (final product)
Data sources:
  Open street maps roads
  NAID aerial imagery (2011)
  Hillshading from USGS DEM

## Slide 16: Results-Morphometry
Full Volume | ~130,000 acre-feet (Error discussion next slide!)
Shoreline length | 109 miles
Shoreline development | 8.87 (bias-corrected 6.17)
Mean Depth | ~16.5 feet
Area | 7830 acres
Water residence time
Vollenweider trophic state
Littoral area
Thermal stability
CEQUAL-W2 model
Etc.

## Slide 17: Results-Error discussion
Area | ~+200 acre-feet
Wind/wave | 1500 acre-feet
Reservoir elevation | 1500 acre-feet
“induced storage” | ~+5,000 acre-feet
Transducer offset | ~+2,000 acre-feet
Area | ~+200 acre-feet
Wind/wave | 
Reservoir elevation | 
“induced storage” | ~+5,000 acre-feet
Transducer offset | ~+2,000 acre-feet

## Slide 18: Application
Scientific:
  Habitable volume for fish

## Slide 19: Application
Scientific:
  Habitable volume for fish
  Weekly data collection safety

## Slide 20: Application
Scientific:
  Habitable volume for fish
  Weekly data collection safety
  Future: Oxygenation and limnology
https://hurthwaterscapes.com/oxygen-saturation-technology/
Notes:     <say we want to calculate fish habitat volume and compare strategies: keeping IPR full vs. oxygenation vs. both>
    Useful for contractors

## Slide 21: Application
Public information dissemination
  Avenza map

## Slide 22: Application
Public information dissemination
  Avenza map

## Slide 23: Application
Public information dissemination
  Avenza map

## Slide 24: Application
Public information dissemination
  Avenza map

## Slide 25: Application
Public information dissemination
  Avenza map

## Slide 26: Application
Public information dissemination
  Avenza map

## Slide 27: Application
Public information dissemination
  Avenza map
  Dynamic map on IP reservoir data website
Notes:   <show dynamism with declining water level>
    One-stop shop for water level, water quality, maybe health advisory information too?

## Slide 28: Application
Public information dissemination
  Avenza map
  Dynamic map on IP reservoir data website
  Angling
Notes:   <show dynamism with declining water level>
    One-stop shop for water level, water quality, maybe health advisory information too?

## Slide 29: Application
Public information dissemination
  Avenza map
  Dynamic map on IP reservoir data website
  Angling
  Safe recreation
Notes:   <show dynamism with declining water level>
    One-stop shop for water level, water quality, maybe health advisory information too?